## Slide 1: Design Document for ASEE robotics competition
Sponsor: Michael Golub, IUPUI Department of Mechanical Engineering migolub@iupui.edu
Group Members: Blake bennett, dallas thornton, glenn haag, torben eid 4/27/2018

## Slide 2: Project motivation
Increase the interest in Robotics at IUPUI.
Increase the reputation of IUPUI Robotics.
Educate underclassmen in the principles of robotic design.
Blake Bennett

## Slide 3: Project background information
American Society of Engineering Education (ASEE) hosts a yearly competition.
An autonomous robot will mimic a worker bee collecting honey in a hive.
Points will be awarded based on the number of ping pong balls correctly placed in the corner pockets.
  10 for correct placement, 5 for incorrect corner placement
2018 ASEE Competition Track
Blake Bennett

## Slide 4: ASEE Competition track
Blake Bennett

## Slide 5: Technical requirements and Constraints
Robot SHALL be completely autonomous.
Robot SHALL retrieve all 13 balls on the track without damaging them.
Robot SHALL NOT damage the track in any capacity.
Robot SHALL be at most 8”X12”X10” to start, but may expand during the run.
Teams SHALL NOT use and robotic kits in any capacity.
Total cost of purchases SHALL NOT exceed $400.
Robot SHALL NOT fly or give off emissions of any kind (solid/liquid/gaseous).
Blake Bennett

## Slide 6: Robot Process Flow Diagram
Blake Bennett

## Slide 7: Locomotion
Four Omni-Directional Wheels
  Wheels are placed at 90 degree angles with respect to each other.
  Provides the best turning control and the easiest implementation of software.
Dallas Thornton

## Slide 8
Locomotion Models
Dallas Thornton

## Slide 9: navigation
Memory Mapping with Sensor Backup
  Error checking done using an array of ultrasonic sensors and an MPU6050 (accelerometer, gyroscope, magnetometer).
  Allows for quick completion time, while also allowing the robot to recover from incremental error in mapping algorithm
Dallas Thornton

## Slide 10: Retrieval system
Pincer design
  Two points of articulation on the retriever arm to meet height constraint as well as position the arm over the sorting subsystem.
  Pincer will grab ball and raise to drop the ball into the sorting sub-system’s flipper.
  The pincer is designed such that the inner diameter is exactly the size of a ping pong ball (40mm).
Torben Eid

## Slide 11: Retrieval system
Torben Eid

## Slide 12: Sorting mechanism
Sort and Separate
  TCS3200 Color light-to-frequency converter is used to determine the color of the two different ping pong balls.
  A servo is attached to a cup that will turn to direct the ball to its respective curved tunnel, based on TCS3200 output signal.
  Utilizes a folded tunnel design that mimics the human intestines to conserve space.
  Saves time by sorting all balls before placement.
Torben Eid

## Slide 13: Sorting mechanism
Torben Eid

## Slide 14: Deposit system
Single-ball dumping system
  Each color set is placed in a tunnel that holds all of the balls of that color until all balls have been retrieved.
  One ball at a time will be fed through the hole at the end of the tube to be deposited.
  Servo motors actuate a lever that ejects the balls.
Glenn Haag

## Slide 15: Final Robot design
Glenn Haag

## Slide 16: Robot software diagram
Dallas Thornton

## Slide 17: Robot hardware Block diagram
Blake Bennett

## Slide 18: Hardware and software testing
Blake Bennett
Bluetooth communication for full system testing.
  Serial printing to a monitor for easy debugging and monitoring of sensor values.
Hardware Testing
  Individual Component Testing
  Full System Testing
    Run Program Exhaustively on Practice Field until Hardware Failure
Software Testing
  Run Program Exhaustively on Practice Field until Software Failure
  Vary Ping Pong Ball Position

## Slide 19: Future work
Blake Bennett
Prepare for next year!
  We had little interest from underclassmen and were unable to obtain a mentee team.
  All future effort on this part should be directed at recruiting a team for next years competition.
Improve Deposit Subsystem software
  Currently the deposit system is the weakest part of the software, it is buggy and should be improved in future iterations.
Improve robot speed
  This could result in a complete overhaul of the physical robot design.
  This would be necessary if the robot were going to the competition.

## Slide 20: Questions?